## Slide 1: Sub-pJ per Operation Scalable Computing with the PULP Platform
MCC2017, Uppsala
30.11.2017
Davide Rossi,
davide.rossi@unibo.it
Notes: Traver is not with us any more

## Slide 2: CPS/IoT Hierarchical Processing
NVIDIA V100 815mm2 TSMC12nm
Apple A11 90mm2 TSMC10nm

## Slide 3: Near Sensor (aka Edge) Processing
Battery + Harvesting powered
 a few mW power envelope
Long range, low BW
Short range, medium BW
Low rate (periodic) data
SW update, commands
Transmit
Idle: ~1µW
Active: ~ 50mW
Analyze and Classify
µController
IOs
1 ÷ 25 MOPS
1 ÷ 10 mW
e.g. CortexM
Sense
MEMS IMU
MEMS Microphone
ULP Imager
100 µW ÷ 2 mW
EMG/ECG/EIT
L2 Memory
ULP
Parallel Processor
1 ÷ 2000 MOPS
1 ÷ 10 mW
1 ÷ 25 MOPS
1 ÷ 10 mW

## Slide 4: NSP: A Quantitative View
Image
Voice/Sound
Inertial
Biometrics
Extremely compact output (single index, alarm, signature)
Recognition:
Speech:
Kalman:
SVM:
607 Kbps
INPUT
BANDWIDTH
COMPUTATIONAL
DEMAND
OUTPUT
BANDWIDTH
4.00 GOPS
10 bps
256 Kbps
100 MOPS
0.02 Kbps
2.4 Kbps
7.7 MOPS
0.02 Kbps
16 Kbps
150 MOPS
0.08 Kbps
[*Nilsson2014]
[*Benatti2014]
[*Ioffe2015]
[*VoiceControl]
Parallel worlkoad
COMPRESSION
FACTOR
60700x
12800x
120x
200x
INCEPTION CNN

## Slide 5: Does it Matter?
3x Cost reduction if data volume is reduced by 95%

## Slide 6: NSP on MCUs?
High performance MCUs
Low-Power MCUs
100x
Courtesy of J Pineda, NXP + Updates
1pJ/OP  InceptionV3 @2fps in 10mW

## Slide 7
Parallel Ultra-Low Power

## Slide 8: Outline
Near Threshold Multiprocessing
Non-Von Neumann Accelerators
Aggressive Approximation
From Frame-based to Event-based Processing
Outlook and Conclusion

## Slide 9: Minimum Energy Operation
Source: Vivek De, INTEL – Date 2013
Near-Threshold Computing (NTC):
Don’t waste energy pushing devices in strong inversion
Recover performance with parallel execution
Manage process/temperature variations in NT!!!

## Slide 10: Near-Threshold Multiprocessing
. . . . .
4-stage OpenRISC &
RISC-V RV32IMC
I$B0
I$Bk
NT but parallel  Max. Energy efficiency when Active
+ strong PM for (partial) idleness
DEMUX
L1 TCDM+T&S
MB0
MBM
Shared L1 DataMem + Atomic Variables
DMA + HW SYNCH
Tightly Coupled DMA
And Hardware Sychronizer
Periph
+ExtM
N Cores
1.. 8 PE-per-cluster, 1…32 clusters
PE0
PEN-1
D. Rossi et al., "Energy-Efficient Near-Threshold Parallel Computing: The PULPv2 Cluster," in IEEE Micro, Sep./Oct. 2017.

## Slide 11: ULP (NT) Bottleneck: Memory
“Standard” 6T SRAMs:
  High VDDMIN
  Bottleneck for energy efficiency
    >50% of energy can go here!!!
Near-Threshold SRAMs (8T)
  Lower VDDMIN
  Area/timing overhead (25%-50%)
  High active energy
  Low technology portability
Standard Cell Memories:
  Wide supply voltage range
  Lower read/write energy (2x - 4x)
  High technology portability
  Major area overhead 4x  2.7x with controlled placement
2x-4x
256x32 6T SRAMS vs. SCM
A. Teman et.al., ‘Power, Area, and Performance Optimization of Standard Cell Memory Arrays Through Controlled Placement’,
in ACM TDAES, May 2016

## Slide 12: I$: a Look Into ‘Real Life’ Applications
Applications on PULP
SHORT JUMP LOOP
BASED APPLICATIONS
LONG JUMP APPLICATIONS
LIBRARY BASED
Issues:
Area Overhead of SCMs (4Kb/core not affordable….)
Capacity miss (with small caches)
Jumps due to runtime (e.g. OpenMP, OpenCL) and other function calls
Exixting ULP processors | Latch based I$
REISC (ESSCIRC2011) | 64b
Sleepwalker (ISSCC 2012) | 128b
Bellevue (ISCAS 2014) | 128b
Survey of State of The Art
SCM-BASED I$ IMPROVES EFFICIENCY BY ~2X ON SMALL BENCHMARKS, BUT…

## Slide 13: Shared I$
I. Loi, et.al., "The Quest for Energy-Efficient I$ Design in Ultra-Low-Power Clustered Many-Cores," in IEEE Transactions on Multi-Scale Computing Systems, In Press.
Share instruction cache
  OK for data parallel execution model
  Not OK for task parallel execution model, or very divergent parallel threads
Architectures
  SP: single-port banks connected through a read-only interconnect
    Pros: Low area overhead
    Cons: Timing pressure, contention
  MP: Multi-ported banks
    Pros: High efficiency
    Cons: Area overhead (several ports)
Results
  Up to 40% better performance than private I$
  Up to 30% better energy efficiency
  Up to 20% better energy*area efficiency

## Slide 14: Near threshold FDSOI technology
Body bias: Highly effective knob for power & variability management!

## Slide 15: Selective, Fine Grained Body Biasing
The cluster is partitioned in separate clock gating and body bias regions
Body bias multiplexers (BBMUXes) control the well voltages of each region
A Power Management Unit (PMU) automatically manages transitions between the operating modes
Power modes of each region:
  Boost mode: active + FBB
  Normal mode: active + NO BB
  Idle mode: clock gated + NO BB (in LVT) RBB (in RVT)
D. Rossi et. al., «A 60 GOPS/W, −1.8V to 0.9V body bias ULP cluster in 28nm UTBB FD-SOI technology»,
in Solid-State Electronics, 2016.

## Slide 16: Body Bias-Based Performance Monitoring and Control
Goal:
Compensate the effects of external factors like ambient temperature
Reduce PVT Margings at design time
Improve Energy Efficiency
 Mixed Hardware/Software control loop exploiting on-chip frequency measurement (PMB)
D. Rossi et al., "A Self-Aware Architecture for PVT Compensation and Power Nap in Near Threshold Processors,"
in IEEE Design & Test, Dec. 2017.

## Slide 17
<32-bit precision  SIMD2/4 opportunity
            HW loops and Post modified LD/ST
            Bit manipulations
            Packed-SIMD ALU operations with dot product
            Rounding and Normalizazion
            Shuffle operations for vectors
Extending RISC-V for NSP
Small Power and Area overhead
RISC-V  V1
V2
V3
HW loops
Post modified Load/Store
Mac
SIMD 2/4 + DotProduct + Shuffling
Bit manipulation unit
Lightweight fixed point
V2
V3
Baseline RISC-V RV32IMC
V1
M. Gautschi et al., "Near-Threshold RISC-V Core With DSP Extensions for Scalable IoT Endpoint Devices," in IEEE TVLSI, Oct. 2017.

## Slide 18: What About FP?
The adoption of floating point formats requiring a lower number of bits (smallFloats) can reduce execution time and energy consumption
  Simpler Logic (smaller pj/op)
  Vectorization (smaller execution time)
SW support:
  flexFloat library for emulation of smallFloat format
  Automatic exploration tool to tune precision of individual FP operations for the required application accuracy
Hardware support:
  smallFloat scalar and vector operations
  Casting operations to move data through different FP types
Tagliavini et. A.l, «A Transprecision Floating-Point Platform
for Ultra-Low Power Computing», DATE 2018

## Slide 19: The Evolution of the ‘Species’
 | PULPv1 | PULPv2 | PULPv3
Status | silicon proven | Silicon proven | post tape out
Technology | FD-SOI 28nm conventional-well | FD-SOI 28nm flip-well | FD-SOI 28nm conventional-well
Voltage range | 0.45V - 1.2V | 0.3V - 1.2V | 0.5V - 0.7V
BB range | -1.8V - 0.9V | 0.0V - 1.8V | -1.8V - 0.9V
Max freq. | 475 MHz | 1 GHz | 200 MHz
Max perf. | 1.9 GOPS | 4 GOPS | 1.8 GOPS
Peak en. eff. | 60 GOPS/W | 135 GOPS/W | 385 GOPS/W
 | PULPv1 | PULPv2 | PULPv3
# of cores | 4 | 4 | 4
L2 memory | 16 kB | 64 kB | 128 kB
TCDM | 16kB SRAM | 32kB SRAM 8kB SCM | 32kB SRAM 16kB SCM
DVFS | no | yes | yes
I$ | 4kB SRAM private | 4kB SCM private | 4kB SCM shared
DSP Extensions | no | no | yes
HW Synchronizer | no | no | yes
2.6pj/OP

## Slide 20: Outline
Near Threshold Multiprocessing
Non-Von Neumann Accelerators
Aggressive Approximation
From Frame-based to Event-based Processing
Outlook and Conclusion

## Slide 21: Recovering More Silicon Efficiency
1
> 100
3
6
CPU
GPGPU
HW IP
GOPS/W
Accelerator Gap
SW
HW
Mixed
Throughput
Computing
General-purpose
Computing
<1 pj/OP
Closing The Accelerator Efficiency Gap with Agile Customization
ULP parallel
Computing

## Slide 22: Heterogeneous PULP Cluster
Fixed function accelerators have limited reuse… how to limit proliferation?

## Slide 23: Learn to Accelerate
Brain-inspired (deep convolutional networks) systems are high performers in many tasks over many domains
Image recognition
[RussakovskyIMAGENET2014]
Speech recognition
[HannunARXIV2014]
Flexible acceleration: learned CNN weights are “the program”
Human:
85% (untrained),
94.9% (trained)
CNN:
93.4% accuracy

## Slide 24: Computational Effort
24
Computational effort
  10-class scene labeling on Stanford-BG
  7.5 GOp/frame for 320x240 image (#Op=2 × #MAC)
  260 GOp/frame for FHD
  1050 GOp/frame for 4k UHD
~90% workload is Conv
Origami CNN ASIC
L. Cavigelli et. Al., "Origami: A 803-GOp/s/W Convolutional Network Accelerator," in IEEE TCSVT, Nov. 2017.
What about pooling/FC layers?

## Slide 25: Heterogeneous PULP SoC: Fulmine
CTRL
Line Buffer + Scalable Precision SOP
Fulmine: Hardware Convolutional Engine (HWCE) in the Cluster
~6.9 mm2 PULP chip, 1/2016
4 cores
1 HWCRYPT accelerator
1 HWCE for 3D conv layers
64kB L1, 192kB L2
QSPI (M/S), I2C, I2S, UART
~1514 kGE for the cluster
232 kGE for the CNN HWCE
Crypto Engine  Secure Analytics
SHARED-MEM IF
F. Conti et al., "An IoT Endpoint System-on-Chip for Secure and Energy-Efficient Near-Sensor Analytics,",in IEEE TCAS-I Sept. 2017.

## Slide 26: Heterogeneous PULP CNN Performance
Chart: 
| 1 core | 4 cores vectorized | 16b weights | 8b weights | 4b weights | SW | HWCE
Cluster Performance [Mop/s] | 58.1991 | 455.8929 | 5065.4762 | 9419.0476 | 12704.7619
Chart: 
| 1 core | 4 cores vectorized | 16b weights | 8b weights | 4b weights | SW | HWCE
Cluster Efficiency [Mop/s/mW] | 38.741 | 289.465 | 1298.4971 | 2414.5027 | 3256.7711
Scaled to ST FD-SOI 28nm @ Vdd=0.6V, f=115MHz
PERFORMANCE
ENERGY EFFICIENCY
13 GOPS
3250 GOPS/W
218x
Cluster performance and energy efficiency on a 64x64 CNN layer (5x5 conv)
84x
[Mop/s]
[Mop/s/W]
5x
0.3 pj/OP
Notes: Pulp v3 comes out of the blue here – it’s important to introduce it before – see my previous note

## Slide 27: Outline
Near Threshold Multiprocessing
Non-Von Neumann Accelerators
Aggressive Approximation
From Frame-based to Event-based Processing
Outlook and Conclusion

## Slide 28: Pushing Further: YodaNN1
Approximation at the algorithmic side Binary weights
BinaryConnect [Courbariaux, NIPS15], XOR NET [Rastegari, arXiv16]
  Reduce weights to a binary value -1/+1
  Stochastic Gradient Descent with Binarization in the Forward Path
  Learning large networks is still challenging, but starts to become feasible:
  ResNet-18 on ImageNet with 83.0% (binary-weight) vs. 89.2% (single- precision) top-5 accuracy; and 60.8% vs. 69.3% top-1 accuracy
Ultra-optimized HW is possible!
  Major arithmetic density improvements: MAC  2s compl. & Accum.
    Area can be used for more energy-efficient weight storage
  Storage reduction  SCM memories for lower voltage  E goes with 1/V2
1After the Yedi Master from Star Wars - “Small in size but wise and powerful” cit. www.starwars.com

## Slide 29: SoP-Unit Optimization
Image Mapping (3x3, 5x5, 7x7)
Equivalent for 7x7 SoP
ImageBank
FilterBank
1 MAC Op = 2 Op (1 Op for the “sign-reverse”, 1 Op for the add).

## Slide 30: YodaNN Energy Efficiency
Same area 832 SoP units + all SCM
12x Boost in core energy efficiency (single layer)
0.03pj/OP
R. Andri et. al., "YodaNN: An Architecture for Ultra-Low Power Binary-Weight CNN Acceleration," in IEEE TCAD, In Press.

## Slide 31: Origami, YodaNN vs. Human
Type | Analog (bio) | Q2.9 Precision | Q2.9 Precision | Binary-Weight
Network | human | ResNet-34 | ResNet-18 | ResNet-18
Top-1 error [%] |  | 21.53 | 30.7 | 39.2
Top-5 error [%] | 5.1 | 5.6 | 10.8 | 17.0
Hardware | Brain | Origami | Origami | YodaNN
Energy-eff. [uJ/img] | 100.000(*) | 1086 | 543 | 31
The «energy-efficient AI» challenge (e.g. Human vs. IBM Watson)
Game over for humans also in energy-efficient vision?
Not yet!
  Numbers above assume on-chip storage (1MB binary weights)
  Object recognition is a very basic task!
*Pbrain = 10W, 10% of the brain used for vision, trained human @ 10img/sec

## Slide 32: Outline
Near Threshold Multiprocessing
Non-Von Neumann Accelerators
Aggressive Approximation
From Frame-based to Event-based Processing
Outlook and Conclusion

## Slide 33: Back to System-Level
Event-Driven Computation, which occurs only when relevant events are detected by the sensor
Event-based sensor interface to minimize IO energy (vs. Frame-based inteface
Mixed-signal event triggering with an ULP imager with internal processing AMS capability
PULPv3
GrainCam
Mixed-Signal Event-based Imager
Digital Parallel Processor
Smart Visual Sensor idle most of the time (nothing interesting to see)
A Neuromorphic Approach for doing nothing VERY well

## Slide 34: GrainCam Imager (FBK)
Pixel-level spatial-contrast extraction
Analog internal image processing
Contrast Extraction
Motion Extraction, differencing two successive frames
Background Subtraction, differencing the reference image, stored in the memory, with the current frame

## Slide 35: GrainCam Readout
Readout modes:
  IDLE: readout the counter of asserted pixels
  ACTIVE: sending out the addresses of asserted pixels (address-coded representation), according raster scan order
Event-based sensing: output frame data bandwidth depends on the external context-activity
Frame-based
{x0, y0}
{x1, y1}
{x2, y2}
{x3, y3}
{xN-1, yN-1}
Event-based
Ultra Low Power Consumption e.g. 10-20uW @10fps

## Slide 36
Power Management
Graincam
IDLE
PULP
Deep Sleep
#events > threshold
Switch to ACTIVE
ACTIVE
Deep Sleep
10μW @10fps
7μW
READOUT
Wake-up
event
Data Trasfer
Data
event
Processing
10-20μW @10fps
2.88 mW Active Power @ 0.55V , 81MHz
Graincam
PULP
M. Rusci, et. al., "A Sub-mW IoT-Endnode for Always-On Visual Monitoring and Smart Triggering," in IEEE IoT Journal, 2017.

## Slide 37: Event-Driven Binary Deep Network
Interger Input Layer
Output Layer
Binary Input Layer
Output Layer
Binary Neural Network (BNN)
Event-based
Binarized Neural Network
Digital Signal Processing
Mixed-Signal Sensing
Integer data
binary data (events)
Spatial-local filtering and binarization
Digital pixel sampling
Layers with binary inputs and binary weights
Imager

## Slide 38: Preliminary Results
300 – 800 µW
3 Classes:
  Pedestrians
  Bikes
  Cars
84.6% vs. 81.6% Accuracy

## Slide 39: Outline
Near Threshold Multiprocessing
Non-Von Neumann Accelerators
Aggressive Approximation
From Frame-based to Event-based Processing
Outlook and Conclusion

## Slide 40: PULP: Parallel Computing For The IoT
The output of our research on PULP is open source
(Solderpad License)
Compiler Infrastructure
Processor & Hardware IPs
Virtualization Layer
Programming Model
Low-Power Silicon Technology

## Slide 41: UNIBO and ETHZ Released PULPino
PULPissimo will be released in few weeks!

## Slide 42: PULP Users And Collaborations
TO BE RELEASED
RELEASED
C
U
7 UNIVERSITIES
10+ COMPANIES
...they are growing …and growing
0%
10%
100%

## Slide 43: Conclusion
Near-sensor processing  Energy efficiency requirements: pJ/OP and below
  Technology scaling alone is not doing the job for us
  Ultra-low power architecture and circuits are needed
CNNs-based visual functions can be squeezed into mW envelope
  Non-von-Neumann acceleration
  Very robust to low precision computations (deterministic and statistical)
  fJ/OP is in sight!
More than CNN is needed (e.g. linear algebra, online optimizazion)
Open Source HW & SW approach innovation ecosystem

## Slide 44
Thanks for your attention!!!
www.pulp-platform.org
The fun is just at the beginning...